## Slide 1
Chin Tong Thia
R6 Kick-Off
Last Updated: 24 June 2019

## Slide 2
Design Methodology
Design Flow in DESENV
Centralized CDC / Lint Signoff
RTL Power Optimization
Review Flow
FPGA Flow
Regression Flow
Agenda
Introduction
Technology Library & Package
Schedule Overview
New/Critical IP Developments
Backend – Physical Partitions
Package Design / IR Drop / Thermal
Analog Design
AMBA/GRFC Interconnect

## Slide 3
R6 is the next generation camera SoC with NPU.
It supports 8MP HDR @ 24fps sensor input, perform various video processing and analytics, and encode up to 8MP@24fps (AV1) + 4MP@24fps (H.264)
Features Highlights
  AV1 – IP for 4K video encoding (Key customer requirement)
  CPU – Improved CPU performance with upgrade from A5-Cortex to A32-Cortex.
  ISP – Improved features and reduced power consumption
  NPU2.0 – Improved power consumption by 40% (~2.4TOPs/W), and increased capacity by 2X (2.4TOPs)
  Security – Added advanced cyber-security features, including TrustZone, OTP, secure boot, and crypto-engines
  SFC – Improved to support up to 100MHz to speed up firmware download speed
Introduction

## Slide 4
Process:
  TSMC 22nm ULP
  1P8M (try to go for 1P9M for smaller die size)
  Only 0.9V and 1.8V devices can be used
  Core voltage: 0.81V to 0.99V, nom=0.9V
  SRAM voltage: 0.81V to 0.99V, nom=0.9V
  IO voltage: nom=1.8V or 3.3V
  Junction Temperature: -40C to 125C, nom=25C
  Ambient Temperature: -40C to 85C
  ESD: 2KV HBM, 500V CDM
Power Domains
  Single Power Domain
Packaging
  256 ball package (non-stack DDR)
  169 ball package (stack LPDDR3)
Technology Library & Package

## Slide 5
Schedule Overview
July
Aug
Sep
Oct
Nov
Phase 2
Phase 3
Phase 1
Phase &
Milestones
Final Netlist *
2nd Netlist
NTO
Backend
Module Design, Verification, Implementation flow
Specification Finalization
Chip Intgn & Env/Tests Build
Finalize macros, die size by end of Phase 1
Use Case HW Emulation
Regression (Module & Chip)
Coverage Analysis
Trial Post-layout simulation
Power Analysis
RTL Freeze Review
Final Post-layout Simulation
NTO Review
Floorplanning & Pad Ring Design
Full trial P&R Flow
Timing closure and Physical Verification Pipe-clean
IR drop analysis
Postlayout netlists/spef release for simulation
FPGA environment and board preparations
Firmware design / modifications
Final P&R Flow
Final Timing closure and Physical Verification Pipe-clean
IR drop sign-off
Final postlayout netlists/spef
NTO Review
Module and chip-level FPGA validation (High and mid-priority usecases)
RTL Freeze Review
Low priority usecases FPGA validation
Schematics design/simulation
Specification Finalization
Release of .v,.lib,.lef by end of Phase 1 with freezed footprint, interface and timing budget
Layout
Postlayout simulation
Release final .v, .lib, .lef by end of Phase 2
Analog Design Freeze Review
SI/PI Simulation (Electrical Testing)
Final post-layout simulations
Analog Design NTO Review
Final GDS by 2/15
Release updated .lib with postlayout signoff timing
Frontend
Analog
Design
Constraints Build
Chip-level and partition synthesis, DFT insertion
Constraints clean-up
Design Flow Pipe-clean
Final Design Flow
Dec
Jan
Feb
Mar
FPGA
Design Flow
1st Netlist
Includes all partitions’ netlists (except VA_processor, CPU and AV1)
VA_processor and CPU netlists to be released earlier in mid-Nov
AV1 would be released on 1/3/20

## Slide 6
IP | Owner(s) | Milestones |  | Outstanding Issue
AV1 | Yuguo, Wayne, Hitoshi, JasonX, Angel, WW | C-Model RTL Complete RTL Freeze | 7/31 8/16 12/31 | New feature impact analysis and resolution – Team is studying it. Milestones need to be confirmed.
NPU2.0 | Wayne, CT, WJ | RTL Complete RTL Freeze | 8/15 11/15 | TOPs requirements – Tentative at 2K MAC@600MHz. Algo team checking high-accuracy OD requirements with YOLOv3 at 608x608
Secure IPs | Stiger, Jason, CT, Florent | RTL Complete RTL Freeze | 9/30 12/12 | On-going spec clarifications with Stiger
ISP | Vince, CT, Thomas, Jeff | C-Model RTL Complete RTL Freeze | 7/31 9/30 12/13 | On-going evaluation new ISP feature requests. Milestones need to be confirmed.
TrustZone | CT, Jason, Florent | RTL Complete RTL Freeze | 9/30 12/13 | 
A32 | Yuguo, Alan, CT, Florent | RTL Delivered RTL Freeze | 7/31 11/15 | Pending license agreement and delivery from ARM Milestones need to be confirmed.
YUVDNS | Wayne, CT, WM | C-Model RTL Complete RTL Freeze | 7/15 9/30 12/13 | Pending algorithm – Wayne plan to study ISP’s raw-DNS for reference/reuse. Milestones need to be confirmed.
YUVSCALE_DN | Wayne, Jason, Shirley | C-Model RTL Complete RTL Freeze | 7/15 9/30 12/13 | Pending algorithm – Wayne plan to evaluate existing algorithm in YUVSCALE but require support to prepare/run the images for subjective testing. Milestones need to be confirmed.
New/Critical IP Developments

## Slide 7
ISP (4M)
Backend - Physical Partitions
Datapath (5M)
RGBIR
RAW
Scaler
ECIF
CB
MERGE
MIPICIF
ISP
DCPC
YUV
Scaler x 5
OSD x 2
VIF x 2
V4
IMG
AV1 (6M)
AV1
Datapath
CPU (3M)
CPU
(A32)
VA_Processor (7M)
NPU
HOGMD
PPU
IAA
Auto-scaler
System Modules (4M)
Peripherals (1M)
Central SRAM
DDR Controller
DMA
CRYPT
GUNZIP
USBD
SFC
SCIF
SCIO
NAND
UART x 2
SCCBM x 2
SIF x 3
PWM x2
WDT x2
Timer x6
AI x 2
MIPIRX
MIPITX
Hard Macros (Partitions)
GIRSTAT
3D-DNS
IDC
SFB x 3
Legend
SBOOT
YUVDNS
From AB1 backend experience, the R6 design partitions need to be more evenly distributed, and the top-level logic needs to keep within 5M gates.
The limit of each partition should be kept within 7M.
This would allow better utilization of licenses/resources and reduce top-level run-time.
- Kevin / CT / Florent

## Slide 8
For R6, the size is almost 2X of AB1. There are challenges on the power consumption and IR drop.
Requires similar technique as R5 (drop power pad in the core area) to meet our IR drop
This would impact the stack package design, and needs to be studied in more details
Need to complete the study by 8/31, when the first netlist is ready.
- Hongyi / Yuguo / Kevin / CT
Package Design / IR Drop / Thermal

## Slide 9
Except for DDR PHY & Audio Codec, the rest of the analog design IP should be reused (except for bug fixes), including the layout.
This allows the LIB and LEF files of the reused IP to be ready now, and avoid re-simulation of postlayout.
- Daniel Liu / APL (to be appointed)
Analog Design

## Slide 10
The AMBA/GRFC interconnects, including memory map decoding would be auto-generated this time round.
Some partitions (e.g. Datapath and VA_processor) are cluster of modules, and would have its own AHB register decoder that has independent clocking. This is to relieve long timing paths connecting all the masters and slaves in the full chip.
To support TrustZone & 128bit AXI.
- Florent / CT / Jason
AMBA/GRFC Interconnects

## Slide 11
The methodology documents are placed in $svn_dir/r6/trunk/hw/doc/methodology
Design Methodology
RTL Design Methodology
ots_design_methodology.pdf
SV Interface Methodology
Coding Rules & Guidelines
Register Design Generation
Module Implementation Flow
ots_implementation_methodology.pdf
run_genus
run_dc
run_pt
run_ccd
run_lec
run_fm
run_ts
run_ppro
Verification Methodology
ots_verification_methodology.pdf
Verification Flow
Coding Rules & Guidelines
Verification Planner
DESENV
Regression Flow
Formal Verification Flow
UVM standard class extension
UVM SOC Framework Flow
HW Emulation Flow
Digital Analog Co-sim Flow
SOC CPU Chip level Verification Environment Usage

## Slide 12
.. for both module and chip-level
Design Flow in DESENV
config.prj
DUT.f
SDC
*_custom_config.tcl
(optional)
run_genus
run_dc
run_lec
run_fm
run_pt
setcfg $MODULE
Designer Inputs
run_spy
Project Config
Synthesis
CDC & Lint
Logic Equiv.
STA
Power Est.
Distilled Reports & Logs
Standardized flow for each tool
Pass / Fail
run_ts
run_ppro
DFT Insertion

## Slide 13
Similar as AB1 and R3LC, there would be centralized CDC / Lint run at full-chip level. This would be used for signoff
However, for faster turnaround, IP owner should clean their IP at module level using the DESENV design flow. The waivers can be reused at chip-level.
- CT / WM
Centralized CDC / Lint Signoff

## Slide 14
With the new Mentor PowerPro (if we manage to purchase it), IP owner should use “run_ppro” in the DESENV design flow to perform RTL structural analysis and pattern-based power analysis to optimize their power
PowerPro attempts to identify non-observable toggling to gate-off, i.e. those logic that are toggling but not captured by any FF. Conceptually, it is as below: If the selector of the mux choose the source from FF_A, the FF_B can be gated off (save clock power, and toggling of the logic cone from FF_B).
- With Mentor PowerPro
RTL Power Optimization

## Slide 15
Reviewers are assigned upfront and needs to sign-off by end of Phase 2 (RTL Freeze)
Review Checklists are placed in $svn_dir/ab1/trunk/hw/doc/reviews
  Module Reviews
  Chip-level Reviews
All Modules (including 3rd party IP, hard-macros) needs to be reviewed.
- CT / Florent / Jason
Review Flow

## Slide 16
Hardware Setup Input Requirements
  PRD/​Chip Spec -- need include datapath and gate count information
  Design change list
Module level FPGA verification
  Covered by IC design team, but the hardware platform only support peripheral verification. For the data path related modules, it will be covered by chip level FPGA verification.
Chip level FPGA verification and SW Validation
  Covered by SOC Integration (SW).
System level FPGA verification
  SOC Integration (HW) will decide the verification scope based on the available resource.
- Frank / HY / Michelle / CT / WW
FPGA Flow

## Slide 17
DESENV Version
  Use http://10.3.2.4/svn/desenv/branches/desenv_r6 (to be updated)
Cadence Simulator with Mentor VRM
Emulation Friendly Verification Environment
  Use UVM (both module and chip level)
Regression to start 2 weeks after 100% RTL (2nd netlist milestone)
Frequency: Twice weekly
- Florent / Toan
Regression Flow

## Slide 18
Checking into main trunk requires users to ensure the following are clean:
  run –t sanity –tl TESTLIST.common (MUST)
  run_genus –link (good-to-have)
  run_vivaldo –link (under development, good-to-have)
This is to make sure the main trunk is not broken. However, it might be time consuming to perform all the above checks if the users simply want to do SVN check-in for regular version control purposes, or for verifiers to test certain bug fixes.
Branching overcome this problem, by allowing users to check-in as they want without affecting the main trunk. They can pull new updates from the main trunk anytime he needs, and merge the changes he made in the branch back to the main trunk when it is cleaned.
Note that after the merge into the main trunk, the branch CANNOT be used anymore. User need to create a new branch for further development
Version Control Flow
Development Branches
Main Trunk
branches/r6_userA_dev0
branches/r6_userB_featureX
trunk
BRANCH
SYNC MERGE
MERGE
BRANCH
MERGE
BRANCH
> svn copy $svn_dir/r6/trunk \
$svn_dir/ab1/branches/r6_userA_dev0 \
-m "Creating a branch of r6/trunk."
> cd $my_working_dir/r6/branches
> svn co $svn_dir/r6/branches/r6_userA_dev0
SYNC MERGE
> cd $my_working_dir/ab1/branches/r6_userA_dev0
> svn merge $svn_dir/ab1/trunk
> svn ci –m “Merging trunk into branch”
MERGE
> cd $my_working_dir/r6/trunk
> svn merge --reintegrate $svn_dir/r6/branches/r6_userA_dev0
> svn ci –m “Merging branch into trunk”
Examples